## Slide 1: Data Acquisition and Transmission
Temperature Sensing of a 3D Printer‘s Hotend
Metin Oktay Yılmaz

## Slide 2: Contents:
Job Description and Definitions
Requirements
Component/Architecture Selection and Their Characteristics
Feasibility Study
Findings / Discussion

## Slide 3: Job Description & Definitions
Short description: Sense the temperature of a 3D printer’s hotend
with a PTC1000 thermistor
Hotend
PTC1000
Heater Block
10 mm

## Slide 4: Requirements
 | a | b
1 | Size: Max 3x3x3 mm | Accuracy: ± 1 ◦C
2 | Weight < 2 grams | Voltage Divider Architecture
3 | Measurement range: 20 - 270 ◦C | Power consumption < 50 mW
4 |  | ADC: 10 bits resolution, 0 - 5V range, rounding-based

## Slide 5: Voltage Divider

## Slide 6: Component Selection
www.te.com
www.microchip.com*
*Microchip acquired Atmel in 2016

## Slide 7: Component Selection: Atmega328PB
www.microchip.com*
*Microchip acquired Atmel in 2016
 | Specifications
1. | 1. 10-bit Resolution
2. | Rounding based schema
3. | ±2 LSB Absolute Accuracy
4. | Up to 76.9 kS/sec (Up to 15 kS/sec at max resolution)
5. | 0 - VCC ADC Input Voltage Range
6. | 3.41 $/unit

## Slide 8: Component Selection: TE PTC1000
www.te.com
 | Specifications
1. | DIN EN 60751 compatible
2. | From -50 to +600 °C
3. | Low resistance drift over lifetime
4. | Fast response time thanks to low thermal mass
5. | 1.76 $/unit
Figure: Voltage across the sensor in the voltage divider

## Slide 9: Feasibility Study: Electrical Requirements
www.te.com
Figure: Voltage across the sensor in the voltage divider
Requirement 4b
Requirement 1b
Requirement 1b: 1°C/step
Requirement 4b: 0 – 5V range

## Slide 10: Power Consumption
Requirement 3b: <50 mW
Requirement 3b
Ω
Ω

## Slide 11: Result
Physical requirements are met.
Electrical requirements are, except for one, met.
Due to the unmet requirement of accuracy, which is caused by ADC resolution, this project is not feasible.